## Slide 1: Slot Car Pilot

## Slide 2: Overview
Visualize
1. Reconstruct Track
3. Optimize Power Control
2. Localize Slot Car

## Slide 3: Reconstruct Track
Lap Detection
Input:
  Drive a couple of rounds
  Use rotation of Slot Car, i.e., z-axis of gyrosensor
Detect laps:
  Autocorrelation of gyro sensor
1. lap

## Slide 4: Reconstruct Track
Shape Estimation
Extract segments:
  Align laps
  Detect curves & straights
Reconstruct track:
Curves sum to 360°
Round to standard segments
1. lap
2. lap
curves
straights
curves

## Slide 5: Localize Slot Car
Compute probability at each track position:
  Update last estimate: Move previous probabilities according to current force value and apply Gaussian blur
  Use sensor measurements: Calculate cross-correlation between gyro values of last second and the track
  Multiply both and scale to 1 to get probability at each track position
gyro values
of last second
Probability at
Each track position
Red dot: most
likely position

## Slide 6: Optimize Power Control
Power control via neural network:
  Extract local track features at most likely position
  Use neural network to compute power value
  Control Slot Car accordingly
Optimize neural network:
  Evaluate parameter settings on track
  Use genetic algorithm to find optimal neural network parameters

## Slide 7: Visualize
A picture is worth a thousand words
Easier to interpret than log files
  Log files are still important!
Your boss likes pictures!